TRI-FLEX II

QUICK REFERENCE GUIDE

Warning: All persons operating this bed must read the entire manual before using the bed.

Procedure for Patient Transport

1. Lower bed to lowest hi-lo position.

2. Remove mattress side bolsters.

3. Release all slide out sections of bed,

and slide in towards bed until locked,

positioning all side rails to the furthest

inward location.

4. Unplug and secure all AC electrical cords.

5. Unlock three casters leaving one foot end

caster locked for steering.

6. Carefully guide bed to new location.

7. Battery back up powers the bed in transit.

Normal Use of Bed

1. Casters should face towards foot of bed with

wheels locked.

2. Cardiac chair position: head & knee up, rev. tren.

3. Bed plugged into AC outlet - powers bed and

continuously charges battery back up.

4. If power outage, battery back up powers the bed.

CPR Instructions         CPR Instructions

1.  Remove head board

2.  Pull red emergency CPR handle under head section

3.  Press “head down” function on hand control.

CPR Instructions         CPR Instructions